A model for the greenhouse effect
[Speaker Notes: ‹#›]

---
THE EXPERIMENT
EXPERIMENTAL MATERIAL:
1 bulb
1 'greenhouse' box: black aluminium plate, plastic lid
1 temperature sensor
1 graphical interface
LP3 software
CHARACTERISTICS AND PHYSICAL ASSUMPTIONS UNDERLYING THE EXPERIMENT:
The T sensor rests on the back of the aluminium plate (the assumption is made that the T is uniform throughout the plate);
The black aluminium plate 'simulates' the earth's surface modelled as a black body;
The plastic lid 'simulates' the atmosphere (making the assumption that it is a uniform layer).
[Speaker Notes: With today's experiments we extend our modelling ... ‹#›]

---
EXPERIMENT in progress
...
GROUP WORK!!!
(20 minutes)

---
From EXPERIMENTS to MODEL
From the cylinders ...
... to the planetary model
From the box ...
... to the Earth-Atmosphere system
[Speaker Notes: FROM EXPERIMENTS TO MODELLING: we now move from reflections on experiments to the interpretation of these from a modelling point of view ... We handled an experimental situation, in which we 'Reflected/Predicted/Interpreted', tried to understand what conditions we were in, what choices were made, what experimental hypotheses (what we selected) ... ...now let us take a step further, let us move from the experiment to the model: from the cylinder experiment to a simple planetary model ... E from the greenhouse box experiment to a planetary model in the presence of an atmosphere ... ‹#›]

---
INTERACTION PROPERTIES
The Earth-Atmosphere System
To understand the role of the atmosphere, consider:
the interaction properties between radiation and matter (a,r,t)
the emissivity ε
Remember: a,r,t and ε vary with wavelength!!!
We will continue to adopt a simplified model and discuss average properties in the short-wave range (SW, 0.3-4 microns) and in the long-wave, or infrared range (LW, 4-50 microns).
This is a simplification!!!
Model 1: a planet without an atmosphere
Model 2: a planet with a homogeneous atmosphere (1 layer)
[Speaker Notes: ‹#› We now look at the parameters a,r,t to see what role an atmosphere around the globe plays. We have already said that these coefficients vary with wavelength ... so to make a simple model we must make a simplifying assumption, i.e. we will take for a,r,t average values in two spectral intervals, one short wave (0.3-4 microns) and a long wave one (4-50 microns), these are two important intervals: the first (the short wave one) coincides with about 99.5% of the radiation that arrives on earth), the second (the long wave one) coincides with 92-93% that a body of typical atmospheric temperature between 200K-330K (a body at that temperature emits in that interval) ... there is a part that emits more in the infrared, but it is not necessary to consider it (we can also say between 4-100 microns) We fix two wavelengths: short wave (0.3-4 microns), which corresponds to the spectral range of solar radiation; long wave (4-50 microns), which corresponds to the spectral range of bodies at a temperature between 200K-330K. (!!) This is a simplification ... because the bodies we have have have different a and r curves (which we instead assume to be constant over the entire range, thus cancelling out the colours) We have already seen one model: PLANETARY MODEL (WITHOUT ATMOSPHERE) which we will now resume ... and then we will introduce a second model in which we introduce an atmosphere (which is, however, uniform, homogeneous, at constant T).]

---
Model 1: planetary climate balance
Under equilibrium (steady-state) conditions, a relationship can be written between the average energy input (solar) and the average energy output.
Emitted radiation power
Absorbed radiation power
Planetary albedo
Radiation from the sun
Sunlit section
Sphere surface (m²)
[Speaker Notes: ‹#› Planetary model: this is a balance equation and tells us that under equilibrium conditions (steady state) as much radiation is entering and as much radiation is leaving ... on the one hand we have: "" We call albedo the part of solar radiation that is reflected back into space; "S' is the radiation coming from the sun (W/m^2) "" is the sunlit section On the other side we have: "" which is the surface area of the sphere (all m^2) times their temperature at the fourth We simplify this equation and derive the T (if we put data, S= 1370 W/m^2, and we put = 0.3 , we get T=255K) ... and we see that the planet without the atmosphere has a T of -18°C (which is more or less the temperature that a body like the moon should have that is without an atmosphere ... although the moon has a higher albedo and is therefore even colder)]

---
Model 1: planetary climate balance
 Te =255 °K
[Speaker Notes: ‹#› We simplify this equation and derive the T (if we put some data, S= 1370 W/m^2, and put = 0.3 , we get T=255K) ... and we see that the planet without the atmosphere has a T of -18°C (which is more or less the temperature that a body like the moon should have that is without an atmosphere ... although the moon has a higher albedo and is therefore even colder)]

---
What are the assumptions/choices made in this MODEL?
We have put ourselves in a state of equilibrium, i.e. it is a planetary balance relationship and therefore identifies a stationary situation.
It can be applied to our planet to identify an average situation over a long period when compared to the period of the Earth's revolution (to eliminate seasonal variations and thus also daily variations).
We considered the Earth as:
a perfectly spherical ball (assumption about its geometric properties);
a black body (a hypothesis on its interaction properties with radiation)
[Speaker Notes: ‹#›]

---
What are the assumptions/choices made in this MODEL?
We considered the radiation of the body as if it were irradiated perpendicularly by a light ray with a cylindrical cross-section of radius equal to that of the Earth (geometric hypothesis)
We have made a global average of the energy absorbed by the body (e.g. being a spherical surface at the poles the net energy input is lower than at the equator) and also a global average of the energy emitted.
We put ourselves in the absence of atmosphere
Assumptions that we will 'unlock' in the next model!
[Speaker Notes: (read hypothesis in the slide) This model (like any model) does not describe the reality of the phenomenon to me, but ultimately gives me a true estimate of what the earth's temperature would be in the absence of an atmosphere (255°K). Why does it 'work' to do this? Making a model means selecting what information is necessary/fundamental to explain a given situation ... (e.g. if we think back to our experiment, if I heat the cylinder with the light bulb, I am interested in the "colour" information, but if I heat it by putting it on a cooker, I am no longer interested in that type of information) ... and so in our modelling we have selected the information we were interested in to estimate the temperature at the earth's surface (in the absence of atmosphere), making explicit our choices, our HYPOTHESIS ... ... that we can work on in order to complexify our model. ‹#›]

---
Model 2: role of an atmosphere
The presence, around a planet, of an atmosphere that interacts with e.m. radiation. , while not changing the balance between incoming and outgoing radiation, substantially changes the average temperature of the layer and the surface.
Hypothesis
SW incoming radiation does not change (assume solar constant)
The outgoing radiation does not change because we are in equilibrium!
(micron)	a / (atm)	a / (sup)	r
0.5 (SW)	0	1	0
10 (LW)	1	1	0
In the SW, the atmosphere is transparent
In the LW it is completely absorbent
[Speaker Notes: ‹#› Role of the atmosphere: if we place an inert atmosphere (i.e. made up only of non-absorbing gases, such as oxygen and nitrogen), i.e. one that is 'transparent' to both solar and infrared radiation ... then it would be like having no atmosphere at all Consider an atmosphere that in short wave is transmitting and the earth's surface is absorbing; while in long wave both the atmosphere and the earth are absorbing (if it absorbs everything, it also emits everything) This is not an easy concept to understand: the radiation coming in from the sun is always the same (obviously assuming that the solar constant is constant), the radiation coming out of the system is always the same because we are in a steady state, otherwise there is no more equilibrium ... even though the same amount of energy is coming out into space, the temperature of the atmosphere and the surface of the Earth changes.]

---
Model 2: role of an atmosphere (aatm=1)
The thermodynamic equilibrium hypothesis allows us to calculate the emissivity: ε = a
System energy balance (sup+atm)
Surface energy balance
[Speaker Notes: ‹#› Now we write the two balance equations to know our two unknowns (the mean T at the top of the atmosphere and the T of the Earth's sup) ... considering that a(atm)=1 ... i.e. behaves like a black body in the infrared!!! T(sup)=303K!!! (that's high!!) The limitation of this model is that NOTHING OF THE RADIATION EMITTED FROM THE TERRESTRIAL SURFACE IS TRANSMITTED INTO SPACE... ALL THAT GOES INTO SPACE IS THAT EMITTED FROM THE ATMOSPHERE, which has its own temperature and emits into space! The assumptions underlying the modelling are: The net radiation entering the atmosphere is considered to be equal to: , where is the total radiation flux from the sun, i.e. the energy coming from the sun per unit of time and unit area, and is the planetary albedo, i.e. the portion of radiation that is reflected by the atmosphere and the planet's surface; the Earth is assumed to emit as a black body, thus following the Stefan-Boltzmann law (), where is the temperature of the Earth's surface; The atmosphere is considered to be transparent to short radiation (SW) and to absorb long radiation (LW ); it is assumed, as a first approximation, that the atmosphere can be represented as a single, physically and chemically homogeneous layer. Reasoning in terms of the energy balance between incoming and outgoing radiation, the two balance equations can be written: at the outer surface of the atmosphere (a) and at the earth's surface (b).]

---
Model 2: role of an atmosphere (aatm=a)
(micron)	a / (atm)	a / (sup)	r
0.5 (SW)	0	1	0
10 (LW)	a (*)	1	0
Thermodynamic equilibrium ε = a
(*) 0< a<1
System energy balance (sup+atm)
Surface energy balance
[Speaker Notes: ‹#›]

---
System balance (sup+atm)
Radiation emitted from the Earth and transmitted from the atmosphere into space
Radiation emitted by the atmosphere
Solar radiation
SUP.
ATM.

---
Balance at the earth's surface
Radiation emitted by the Earth
Radiation emitted by the atmosphere
towards the Earth then absorbed by the Earth)
Solar radiation
SUP.
ATM.

---
Model 2: role of an atmsphere (aatm=a)
a / (atm for LW)	TA / (°K)	TS / (°K)
0	214.4	255.0
0.5	230.4	274.0
0.7	238.8	284.0
1	255.0	303.3
As 'a' increases, the temperature of the atm and sup increase, in order to maintain the balance with incoming radiation.
In this case, it is only the Atmosphere that contributes in sending the radiation into space.
In this case, it is only the Earth that contributes in sending radiation into space.
[Speaker Notes: ‹#› What are the limitations of this model: Assume that the atmosphere is homogeneous (this is not true because the densities of gases vary in the atmosphere, they are denser near the ground usually ... although not all of them, e.g. ozone absorbs more in the upper atmosphere) ... in general the gases that absorb in the infrared decrease with altitude The atmosphere does not have a uniform temperature ... T varies with altitude, so an object that has temperatures inside it that vary a lot is not in thermodynamic equilibrium ... so ours is a first approximation ... we can then, for example, make a second-order approximation by stratifying the atmosphere ... so we can go and complexify our model by changing our constraints]

---
Limitations of this model
It is assumed that the atmosphere is homogeneous and has only one temperature.
It does not include the fact that in a real atmosphere, gases have densities that vary with altitude and temperature also varies with altitude.
Moreover, the atmosphere as a whole is NOT in thermodynamic equilibrium.

---
Assumptions/simplifications underlying the model
(consider that climate is not such a simple thing)
our calculations predict a homogeneous planet
we are making global average forecasts
we are assuming that absorbance is averaged over only two intervals (short wave and long wave)
carbon dioxide is assumed to be evenly distributed over the entire globe, but water vapour decreases as it moves towards the polar regions, so absorbance decreases
there are feedback effects (melting ice decreases planetary albedo, so if albedo decreases, absorbance increases ... and this is positive feedback, i.e. it goes in the direction of increasing the effect)

---
GRAPHICS

---
Greenhouse WITHOUT lid

---
Greenhouse WITH lid

---
The 'climate' is a complex system!
It is the result of the interaction between the atmosphere and the Earth system, it is therefore composed of many (and different) sub-systems.
(taken from the 2001 WG1-IPCC report)
[Speaker Notes: There is no single definition of complexity and complex system ... In general, what characterises a complex system can be: - sensitivity to initial conditions, which in some cases leads to unpredictability of its future state; - the fact that the superposition principle does not apply to it (i.e. that the final effect of two causes here is not the sum of the effects caused by each cause taken individually); - the presence of feedback, i.e. the fact that there are circular cause-effect chains in which the last effect in the chain goes on to influence the first cause from which the chain itself started, modifying it. ‹#›]

---
There are some important considerations to be made ...
The 'recomposition' of the parts does not return the total system in a linear manner, as the interaction between the parts produces feedback effects:
Positive feedback: if it adds to the first cause
Negative feedback: if it dampens the cause first

---
REFLECTION ...
What is the added value that the laboratory can provide in an educational course? But also what added value does having to think about experiments in dealing with complex, multi-disciplinary topics, such as climate change, provide to the laboratory?
What are the different attitudes one can have when faced with a laboratory? And what is the relationship between experiment, reality, and modelling?
[Speaker Notes: How does the workshop fit into this educational journey and what role does it play? What added value does the laboratory bring to such a multi-disciplinary course? But also what added value does having to think about experiments in such a complex topic as climate change provide to the laboratory? ... I'm getting out of the mechanics ... I don't have to verify a law ... So far I have seen the laboratory as that place where phenomena are 'reproduced' ... But what are the various attitudes one can have when faced with the laboratory? And what is the relationship between experiment, reality, and modelling? ‹#›]

---
Giulia Tasquier
Department of Physics and Astronomy, Alma Mater Studiorum - University of Bologna
giulia.tasquier2@unibo.it